## Slide 1: Cache Memory
I2
By Thavorac

## Slide 2
Computer
Peripherals
CPU
Main Memory
Keyboard
Mouse
Monitor
Speaker
Scanner
Printer
Logical Architecture
Physical Architecture
ISA & Instruction
Addressing Modes
Cache

## Slide 3: Why memory cache is required
Cache memory is important because it improves the efficiency of data retrieval. It stores program instructions and data that are used repeatedly in the operation of programs or information that the CPU is likely to need next.

## Slide 7: Cache operation - Overview
CPU requests contents of memory location
Check cache for this data
If present, get from cache (fast)
If not present, read required block from main memory to cache
Then deliver from cache to CPU
Cache includes tags to identify which block of main memory is in each cache slot

## Slide 9: Cache design
Addressing
Size
Mapping Function
Replacement Algorithm
Write Policy
Block Size
Number of Caches

## Slide 10: Cache addressing
Where does cache sit?
  Between processor and virtual memory management unit
  Between MMU and main memory
Logical cache (virtual cache) stores data using virtual addresses
  Processor accesses cache directly, not thorough physical cache
  Cache access faster, before MMU address translation
  Virtual addresses use same address space for different applications
    Must flush cache on each context switch
Physical cache stores data using main memory physical addresses

## Slide 11: Size does matter
Cost
  More cache is expensive
Speed
  More cache is faster (up to a point)
  Checking cache for data takes time

## Slide 12: Typical cache organization

## Slide 13: Locality of reference
Processors tend to access memory in a very patterned way. if memory location X is accessed at time t, there is a high probability that memory location X + 1 will also be accessed in the near future.
This type of pattern is called “Locality of Reference”. There are other types as well:
Temporal locality—Recently accessed items tend to be accessed again in the near future.
Spatial locality—Accesses tend to be clustered in the address space (for example, as in arrays or loops).
Sequential locality—Instructions tend to be accessed sequentially.

## Slide 14: Cache Mapping Schemes
For cache to be functional, it must store useful data. However, this data becomes useless if the CPU can’t find it
Cache
RAM
2E3
convert
Cache mapping scheme

## Slide 15
Direct Mapped Cache
Direct mapped cache assigns cache mappings using a modular approach. Because there are more main memory blocks than there are cache blocks, it should be clear that main memory blocks compete for cache locations.
In direct mapped cache, a block of main memory has a specific location in cache.
For example, if cache contains 10 blocks, then main memory block 0 maps to cache block 0, main memory block 1 maps to cache block 1, . . . , main memory block 9 maps to cache block 9, and main memory block 10 maps to cache block 0

## Slide 16: excercise

## Slide 17: example
Assume memory consists of 214 words, cache has 16 blocks, and each block has 8 words. From this we determine that memory has blocks.
We know that each main memory address requires 14 bits. Of this 14-bit address field, the rightmost 3 bits reflect the word field (we need 3 bits to uniquely identify one of 8 words in a block). We need 4 bits to select a specific block in cache, so the block field consists of the middle 4 bits. The remaining 7 bits make up the tag field.

## Slide 18
Fully Associative Cache
Direct mapped cache is not as expensive as other caches because the mapping scheme does not require any searching. Each main memory block has a specific location to which it maps in cache
Instead, Fully Associative Cache allows a main memory block to be placed anywhere in cache and searching is done all over the cache.
Example: Consider the memory with 214 words, a cache with 16 blocks and blocks of 8 words.
So we have:

## Slide 19
Set Associative Cache
Associative cache is very expensive and direct mapping is inexpensive but very restrictive.
So there is another method which is a combination of fully associative and direct mapping, the N-way set associative. Instead of mapping a block to specific location in cache, but it map block to set instead.
In set-associative cache mapping, the main memory address is partitioned into three pieces: the tag field, the set field, and the word field.

## Slide 20
Example
Suppose we are using 2-way set associative mapping with a main memory of 214 words, a cache with 16 blocks, where each block contains 8 words. If cache consists of a total of 16 blocks, and each set has 2 blocks, then there are 8 sets in cache.
Therefore, the set field is 3 bits, the word field is 3 bits, and the tag field is 8 bits.

## Slide 21: Effective access time and hit ratio
The performance of a hierarchical memory is measured by its effective access time (EAT), or the average time per access.
For example, suppose the cache access time is 10ns, main memory access time is 200ns, and the cache hit rate is 99%. The average time for the processor to access an item in this two-level memory would then be:
where H = cache hit rate, AccessC = cache access time, and AccessMM = main memory access time.